## Slide 1: NTAF CONFORMANCE TESTS
Elemér Lelik
Ericsson Test Competence Centre
Westford, MA
September 17-19, 2013

## Slide 2: TEST PuRposeS
Test purpose specification: ISO/IEC 9646-1 (Conformance testing methodology and framework, General concepts)
ISO/IEC 9646-2 (Abstract Test Suite Specification)
ETSI ES 202 553 Methods for testing and Specification: TPLan: A notation for expressing Test Purposes

## Slide 3: test purpose specification Example
TP Id | TP_NTAF_TS_001_ACT_RBV_001
Test objective | Check that activation requests sent to an always-on tool are responded with activate result pass
Reference | NTAF TS-001 Activating an always-on tool
Initial conditions | 
with { the IUT being in the "initial state" } | 
Expected behaviour | 
ensure that { when { the IUT receives an activation request for a supported harness and a supported mode from a client } then { the IUT sends an InformationQuery type result containing activate containing result indicating value pass } } | 

## Slide 4: TTCN-3
Standardized test specification language
  Developed and maintained by
Endorsed by without technical changes
C like syntax; built-in test-oriented features( timer handling, test components, templates and a powerful matching mechanism)
Defined interworking with ASN.1, XML, C/C++ etc.
Intensively used by standardization bodies
and in the telecoms and automotive industry
for further info, see: http://www.ttcn-3.org

## Slide 5: Titan
An Ericsson internal test development and execution environment based on the standardized testing language
which includes the full range of features needed for test specification, execution and analysis

## Slide 6: NTAF CONFORMANCE TOOL-BOX
VmWare Virtual machine

## Slide 7: TOOL-BOX CONTENT
Openfire, Pidgin, Wireshark, Firefox, OpenSSH and NxServer, Xmllint
Collection of XMPP, NTAF, TTCN-3 standards
Titan (TTCN-3 compiler & executor) and a set of
conformance test cases written in TTCN-3

## Slide 8: LoGIN
VmWare virtual machine built on Ubuntu 12.04
Username:ntaf
Password:ntaf

## Slide 9: XMPP server
ntaf@ntaf:~/openfire/bin$ ./openfire start
ntaf@ntaf:~/openfire/bin$ ./openfire status
The daemon is running.
ntaf@ntaf:~/openfire/bin$ ./openfire stop

## Slide 10: OPENFIRE CREDENTIALS
admin/ntaf

## Slide 11: STARTING THE TESTS
cd Conformance/bin
../src/install.script
make
ttcn3_start NTAF_exec NTAF.cfg

## Slide 12: Network layout
XMPP Server
NTAF/XMPP Client
NTAF/XMPP Client
VM

## Slide 13: Test scenarios
SUT: NTAF Provider
XMPP Server
NTAF Requestor
VM

## Slide 14: Test scenarios
SUT: NTAF Requestor
XMPP Server
NTAF Provider
VM

## Slide 15: Test Architecture
MTC
mapping
decoding
behaviour
XMPP server
SUT
XMPP/TCP
XMPP/TCP
VM
ntaf.conformance.test:5222

## Slide 16: Simplifying assumptions:
….
ntaf.tools
collection node
leaf node
leaf node
leaf node
harnesses
harnesses
harnesses

## Slide 17: PROVIDER TESTCASE STRUCTURE

## Slide 18: REQUESTOR TESTCASE STRUCTURE

## Slide 19: TEST CASE SKELETON

## Slide 20: ISSUES OUTSTANDING
Review of the test cases, validation against a non-simulated node
Missing test cases (e.g. tests for proxied tools)
Action parameters to be fed as configuration parameters
XMPP Server in TTCN-3 (?)